Section 1---Instruction of Assembling Gas Hose

The gas hose can be changed by the customers if there is a need. Please follow the steps below:

1. Mount the Flange Cap to the Gas Hose.

2.  Install the Pressing Set onto the gas hose.

3.  Make the Flange cling to the pressing set.

4. Screw the flange cap to flange and make sure it is tight enough.

5. Apply epoxy adhesive to glue the Al2O3 ceramic tube and adaptor together.

Note: The customer is advised not to change the Al2O3 tube sticking to the flange.

6. Installation is done

Section 2--- Instruction of Installing the Gas Purging Adaptor

MTI’s muffle furnaces can be easily promoted by installing the gas purging adaptor according to the customers’ special use, please follow the steps below to make it right:

1. Unscrew the Two Screws beside the outlet on the top cover of the furnace:

2.  Put the Al2O3 Tube labeled “outlet” with the flange and gas hose together into the outlet.

3.  Match the screw holes on the flange to the ones beside the outlet, and then tighten the two

screws with Hex Driver.

4. To install the tube labeled “inlet” to the inlet, repeat the steps 1-3.

5. Finish the installation and start to use.

Section 3--- Instruction of Producing Gas Inlet and Outlet

MTI will provide the gas holes and charge certain fees; however, if the customer does it by self,

drilling and tapping tools are required.

1. Produce outlet

a. Drill a hole on the cover; make sure the diameter is a little larger than that of Al2O3 tube.

b-1-1. Properly posit the flange, drill through the cover by the screw holes on the two sides of

flange.

b-1-2. Remove the flange and tapping the two screws holes on the cover according to the

specification of the screws.

b-2.  If you have no idea of how to tap the screw holes, please simply apply glue to adhere

the flange on the cover.

c. Vertically insert the Al2O3 tube through the hole until touch the surface of module and

then mark the touching point to it.

d.  Remove the cover, drilling the touching point with holding the bottom of module in the

chamber in case of module splitting.

f. Do the same hole on the back for gas inlet.

g. Follow section 2 to install the flange and then be ready for using.

MTI Corporation                                                            Website: www.mtixtl.com

860 South 19th Street, Richmond, CA 94804, USA

Tel: (510)525-3070     Fax: (510) 525-4705                     E-mail: info@mtixtl.com

# Text boxes

Drilling the touching point on the module

Drill though the screw hole

Tapping Tool